## Slide 1: SIKE Round 2 Speed Record on ARM Cortex-M4
Hwajeong Seo (Hansung University), SK
Amir Jalali (Florida Atlantic University), USA
Reza Azarderakhsh (Florida Atlantic University, PQSecure Technologies), USA
Presenter: Hyeokdong Kwon (Hansung University)

## Slide 2: Outline
Short Overview
Supersingular isogeny key encapsulation (SIKE) protocol
Our implementation
Implementation results
Conclusion

## Slide 3: Quantum Threat to Information Security
Large-scale quantum
computers could break some encryption schemes
Need to migrate encryption to quantum- resistant algorithms
When we should start the process?
Questions:
When will quantum computers arrive?
When will they be a threat?
When do we switch?
How do we have live and agile transition?
What do we transition to?
…
“In 25 years we’ll be working on quantum resistant crypto standardization based on elliptic curves in some way!”
─Dustin Moody, NIST (NSF CCC Workshop 2019)

## Slide 4: Post-Quantum Cryptography (Isogeny)
Quantum-Resistant Cryptography
  NIST launches the post-quantum cryptography standardization project
“The goal of this process is to select a number of acceptable candidate cryptosystems for standardization.”
  Code, Lattice, Hash, Multivariate, Isogeny…

## Slide 5: Quick Overview
[2006]: Birth of a supersingular isogeny-based cryptosystem
  Charles – Goren – Lauter
  built hash function from supersingular isogeny graph
[2011]: Supersingular isogeny key exchange
  Jao – De Feo
[2017]: Supersingular isogeny key encapsulation
  SIKE Team

## Slide 6: Post-Quantum Cryptography (Isogeny)
Round1 (2017. 12) : 69 accepted as “complete and proper” (5 withdrew)
Round2 (2019. 01) : 26 accepted including SIKE
SIKE Round2
  New parameters: SIKEp434, SIKEp610
  Stronger security: SIKEp503 (12) SIKEp751 (35)

## Slide 7: SIKE Team

## Slide 8: Motivation
Type | Algorithm | Advantage | Disadvantage
Code | McEliece | Fast computation | Long key size
Hash | XMSS, SPHINCS | Security proof | Long signature size
Lattice | (ring)-LWE | Fast computation | Difficulty of parameter selection
Multivariate | UOV, Rainbow | Short signature size Fast computation | Long key size
Isogeny | SIDH, SIKE | Short key size | Slow computation
All PQC candidates have their own pros and cons.
Disadvantage of SIDH/SIKE is slow computation.

## Slide 9: Motivation
In this talk, we address this problem on 32-bit ARM Cortex-M4 processors.

## Slide 10: PQC on Low-end Microcontroller
STM32F4DISCOVERY
  ARM Cortex-M4
  32-bit, ARMv7E-M
  192 KB RAM, 168 MHz
Benchmark framework
  PQM4: github.com/mupq/pqm4

## Slide 11: Previous Works on SIKE/SIDH
64-bit ARM-A processor:
  Jalali et al. [SAC’17]  Seo et al. [CHES’18]  Jalali et al. [TDSC’19] Seo et al. [WISA’19]
32-bit ARM-A processor:
  Koziel et al. [CANS’16]  Jalali et al. [SPACE’18]  Seo et al. [CHES’18]
32-bit ARM-M processor:
  This work [CANS’19]

## Slide 12: Contribution
Optimized finite field arithmetic: super-scalar implementation
Scalable implementation: well scheduled instruction
Efficient Implementation of SIKE:
  p434 (1.94 sec) on 32-bit ARM Cortex-M4 @168MHz

## Slide 13: Outline
Short Overview
Supersingular isogeny key encapsulation (SIKE) protocol
Our implementation
Implementation results
Conclusion

## Slide 14: Isogeny-Based Cryptography
Isogeny-based cryptography is constructed on a set of curves.
Given two curve and find ?

## Slide 15: Post-quantum key exchange algorithm
Supersingular Isogeny Diffie-Hellman (SIDH)
  Shared key generation between two parties over an insecure communication channel.
  SIDH works with the set of supersingular elliptic curves over and their isogenies.

## Slide 16: SIDH Computations

## Slide 17: Supersingular Isogeny Key Encapsulation (SIKE)
SIDH is not secure when keys are reused (Galbraith-Petit-Shani-Ti 2016)
SIKE: IND-CCA secure key encapsulation based on SIDH.
Uses a variant of Hofheinz–Hövelmanns–Kiltz (HHK) transform: IND-CPA PKE → IND-CCA KEM
Starting curve : , (Round 1) switched to : (Round 2),
where

## Slide 18: SIKE Key sizes
NIST Level | Prime size (bits) | Prime | Public key size (bytes) | Compressed PK size (bytes)
1 | 434 |  | 330 | 196
2 | 503 |  | 378 | 224
3 | 610 |  | 462 | 273
5 | 751 |  | 564 | 331
NIST Level | Prime size (bits) | Prime | Public key size (bytes) | Compressed PK size (bytes)
1 | 434 |  | 330 | 196
2 | 503 |  | 378 | 224
3 | 610 |  | 462 | 273
5 | 751 |  | 564 | 331

## Slide 19: Outline
Short Overview
Supersingular isogeny key encapsulation (SIKE) protocol
Our implementation
Implementation results
Conclusion

## Slide 20: Multiplication Instruction (32-bit ARMv7)
a0
b0
a0b0 + c0 + d0
R0
R1
R3, R2
32 bits
64 bits
c0
R2
d0
R3
UMAAL R2, R3, R0, R1

## Slide 21: Comparison of Multiprecision Multiplication (32-bit ARMv7-M)
Consecutive Operand Caching (COC)
Operand Scanning (OS)
Proposed Refined Operand Caching (ROC)
Requirements for ROC  More registers

## Slide 22: Comparison of Register Utilization

## Slide 23: Comparison of Performance
The number of memory access is significantly reduced

## Slide 24: Implementation in Detail
UMULL  Initialize the result registers

## Slide 25: Implementation in Detail
Avoiding the pipeline stall through instruction re-ordering

## Slide 26: Squaring in Detail

## Slide 27: Multiplication/Squaring Result
Multiplication
Squaring

## Slide 28: Modular Reduction
Montgomery Reduction: Division  Multiplication

## Slide 29: Modular Reduction Result

## Slide 30: Modular ADD/SUB
Both carry and borrow catcher

## Slide 31: Modular ADD/SUB Result

## Slide 32: Outline
Short Overview
Supersingular isogeny key encapsulation (SIKE) protocol
Our implementation
Implementation results
Conclusion

## Slide 33: Results
SIDHp503 is about 19x faster than SIDH v3.0 and SIDHp751 is about 2.7x faster than Koppermann et al.

## Slide 34: Comparison with NIST PQC

## Slide 35: Results on all ARM processors

## Slide 36: Outline
Short Overview
Supersingular isogeny key encapsulation (SIKE) protocol
Our implementation
Implementation results
Conclusion

## Slide 37: Conclusion
New implementations of finite field arithemtic on ARM
  Faster multi-precision multiplication/squaring
  Faster Montgomery reduction
  Faster modular addition/subtraction
Record-setting SIDH and SIKE implementations
  On 32-bit ARM Cortex-M4
  Thank you for your attention!