## Slide 1: Optimized SIKE Round 2 on 64-bit ARM
Hwajeong Seo1, Amir Jalali2, and Reza Azarderakhsh2
1Hansung University, 2Florida Atlantic University

## Slide 2
Motivation
Target Platform
Proposed Method
Evaluation
Conclusion

## Slide 3: Motivation
High performance is important to achieve the service availability
The cryptography imposes the high overheads on computers
Furthermore, some PQC standard show low performance
We target SIKE Round 2 curves, such as SIKEp434 and SIKEp610

## Slide 4: Diffie-Hellman Instantiations

## Slide 5: Pre-quantum ECC vs Post-quantum ECC

## Slide 6: Post-quantum key exchange algorithm
Supersingular Isogeny Diffie-Hellman (SIDH)
  Shared key generation between two parties over an insecure communication channel.
  SIDH works with the set of supersingular elliptic curves over and their isogenies.

## Slide 7: SIKE Round 2
SIKE
  One of the PQC candidates
  Hardness of solving isogeny maps between supersingular elliptic curves
SIKE Round 1
  SIKEp503 (NIST 1), SIKEp751 (NIST 3), and SIKEp964 (NIST 5)
SIKE Round 2
  New curves: SIKEp434, SIKEp610
  Security level changes: SIKEp503 (NIST 12), SIKEp751 (NIST 35)
  Excluding SIKEp964

## Slide 8: Target Platform – 64-bit ARMv8-A
95% of smartphones based on ARM architecture
Modern smartphone supports 64-bit ARMv8
  e.g. iPhone and Galaxy

## Slide 9: Target Platform – 64-bit ARMv8-A
32-bit mode (AArch32) & 64-bit mode (AArch64)
64-bit ARM & 128-bit NEON registers and instruction sets
Crypto (AES and SHA) operation

## Slide 10: Multiplication on ARMv8
a0
b0
a0b0
a0b0
X0
X1
X2
64 bits
X3
UMULH
a0
b0
a0b0
a1b0
X0
X1
X2
64 bits
X3
MUL

## Slide 11: Multiplication on ARMv8
a3
a2
a1
a0
b0
b2
b3
b1
a0b0
a1b0
V0
V1
V2
32 bits
32 bits
64 bits
SIMD (NEON)
a0
b0
a0b0
a0b0
X0
X1
X2
64 bits
64 bits
SISD (A64)
64 bits
X3
MUL
UMULH
UMULL
For 64-bit multiplication on ARMv8,
NEON requires 4 UMULL routines but A64 only needs 1 MUL and 1 UMULH.
A64 is more efficient than NEON for big integer multiplication.

## Slide 12: Multi-precision Multiplication
256~2048-bit multiplication on 64-bit architecture
Divide big integer (256~2048-bit) into small integer (64-bit)
ARMv8 supports 31x64-bit registers
Method | Operand-scanning | Product-scanning | Hybrid-scanning
Computation order | Row-wise | Column-wise | Mixture of row/column
Requirement | Many registers | Efficient MAC routine | General processor

## Slide 13: Multi-precision Multiplication (Product Scanning)

## Slide 14: Multi-precision Multiplication (Operand Scanning)

## Slide 15: Comparison between Product-scanning & Operand-scanning
Product-scanning
Operand-scanning
9 additions
8 additions

## Slide 16: Comparison between Product-scanning & Operand-scanning
Number of addition operations depending on the number of limb
  Operand-scanning shows lower number of addition than product-scanning
Method | Number of limb |  |  |  | 
 | 3 | 4 | 5 | 6 | 7
Operand-scanning | 24 | 40 | 60 | 84 | 112
Product-scanning | 27 | 48 | 75 | 108 | 147

## Slide 17: Karatsuba-Ofman Algorithm
Number of partial product
The product of two n-bit integers and
610-bit multiplication uses Karatsuba method
School-book | Karatsuba-Ofman
School-book | Karatsuba-Ofman

## Slide 18: Subtractive Karatsuba Algorithm
=
Advantage:
  constant size of operands (n/2)  fast constant-time multiplication
Requirement:
  Absolute value in two’s complement representation

## Slide 19: Evaluation
Multiplication implementations for SIKEp434 and SIKEp610 are improved by 4.5x and 4.9x, respectively.
Implementation | Language | Protocol | Timing [cc] |  |  | 
 |  |  | Addition | Subtraction | Multiplication | Inversion
SIKE Round 2 | C | SIKEp434 | 172 | 129 | 3,110 | 1,648,372
This work | ASM |  | 71 | 63 | 691 | 380,711
SIKE Round 2 | C | SIKEp610 | 257 | 187 | 6,599 | 4,800,694
This work | ASM |  | 100 | 91 | 1,329 | 963,064

## Slide 20: Evaluation
Total protocols for SIKEp434 and SIKEp610 are also improved by 3.8x and 3.4x, respectively.
SIKEp434 shows the most optimal performance among SIKE curves.
Implementation | Language | Protocol | Timing [cc] | Timing [cc * 10^6] |  |  | 
 |  |  | Multiplication | KeyGen | Encaps | Decaps | Total
SIKE Round 2 | C | SIKEp434 | 3,110 | 114 | 186 | 199 | 499
This work | ASM |  | 691 | 30 | 49 | 52 | 130
Seo et al. | ASM | SIKEp503 | 849 | 38 | 63 | 67 | 168
SIKE Round 2 | C | SIKEp610 | 6,599 | 344 | 634 | 615 | 1,593
This work | ASM |  | 1,329 | 99 | 183 | 183 | 465
Seo et al. | ASM | SIKEp751 | 2,450 | 164 | 265 | 284 | 713

## Slide 21: Conclusion
Achievements
  Efficient implementations of multi-precision multiplication on ARMv8
  First implementation of SIKE Round 2 curves on ARMv8
Future works
  Further cryptography implementations (other SIKE and PQC)