## Slide 1: 블록체인 기반 IoT 내에서의 Quark 연구 동향
김원웅

## Slide 2
서론
관련 연구
연구 동향
결론

## Slide 3: 서론
블록체인 기술이 IoT 분야에서의 보안 문제를 해결하기 위한 솔루션으로 떠오르고 있음
그러나, IoT의 특성상 자원이 제한적이므로 메모리나 전력이 충분하지 않음
  블록체인 기반 IoT의 가용성을 위해 블록체인 경량화에 초점
  블록체인의 경량화를 위하여 적절한 해시 함수를 선택

## Slide 4: 관련 연구 (Quark)
Quark는 경량 암호화 해시함수이며, RFID 상에서의 암호화 프로토콜을 구현하기 위하여 설계됨
Quark는 크게 u-Quark, d-Quark, s-Quark, c-Quark로 나뉨  상황에 따라 선택 가능
각각 64bits, 80bits, 112bits, 256bits의 보안 강도를 가짐
각각 1379, 1702, 2296, 4000개의 GE만을 사용하여 경량 해시함수에 적합함

## Slide 5: 연구 동향[1]
“Scalable Peer-to-Peer Fog Computing Integrated to a Fast-Searching Distributed Blockchain System.”
블록체인 네트워크를 통하여 보안이 보장된 3계층 p2p 포그 IoT를 설계
데이터 검색과 데이터 저장을 모두 지원하며 인증자에 의해 인증된 노드만 IoT 시스템에 참여 가능
인증 ID는 IP 주소와 PUF(Pyshical Unclonable Function) 사용
키-값에 따라 데이터를 매핑  이때 u-Quark를 사용하여 데이터의 크기를 감소시켜 IoT 자원의 제한을 완화

## Slide 6: 연구 동향[2]
“A lightweight hash-based blockchain architecture for industrial IoT.”
산업용 IoT인 IIoT(Industrial IoT)를 위한 경량 블록체인을 제안
블록체인의 고려사항을 분석하여 네트워크 트래픽에 맞춰 마이닝에 사용되는 해시 알고리즘을 변경
Cell node와 Storage node로 구성
  Cell Node는 블록을 생성한 후 검증을 위해 다른 노드들에게 브로드 캐스팅
  Storage Node는 블록의 업데이트를 진행
트래픽 분석기가 트랜잭션의 수를 조사
미리 정의된 임계값에 따라 블록 마이닝을 위한 경량 해시 목록에서 해시 함수를 선택
   경량 해시 목록에는 QUARK, PHOTON, SPONGENT가 포함

## Slide 7: 연구 동향[2]
T: 트랜잭션 처리 시간, dn: 네트워크 통신 지연, D: 블록 채굴 난이도, s: 해시 함수의 처리량
W: 트랜잭션의 크기, dv: 통신 확인 지연, du: 블록 저장을 위한 업데이트 지연, h1, h2: 해시 함수 변경을 위한 임계값
D에 따라서 해시 함수가 결정됨.
  D < h1  s가 11.43인 SPONGENT 사용
  h1 < D < h2  s가 20.51인 PHONTON 사용
  h2 < D  s가 50인 QUARK 사용

## Slide 8: 결론
Quark 경량 해시함수를 적용한 블록체인 기반의 IoT 동향
 SPONGENT, PHOTON과 같은 다른 경량 해시 함수에 비해 비교적 보안 강도가 낮음
 하지만, 최소한의 보안 강도는 만족하며, 전력과 에너지를 적게 소비하여 IoT 환경에 적합하다.

## Slide 9: 참고 문헌
[1] Omar, Michael, and Doan Tung Trung. "Scalable Peer-to-Peer Fog Computing Integrated to a Fast-Searching Distributed Blockchain System." 2021 6th International Conference on Intelligent Information Technology. 2021.
[2] Seok, Byoungjin, Jinseong Park, and Jong Hyuk Park. "A lightweight hash-based blockchain architecture for industrial IoT." Applied Sciences 9.18 (2019): 3740.
[3] David, Shibin, et al. "Augmenting integrity and scalability in mobile payment applications using blockchain." E3S Web of Conferences. Vol. 297. EDP Sciences, 2021.
[4] Abed, Sa’ed, et al. "An analysis and evaluation of lightweight hash functions for blockchain-based IoT devices." Cluster Computing 24.4 (2021): 3065-3084.
[5] Kuznetsov, Alexandr, et al. "Performance Analysis of Cryptographic Hash Functions Suitable for Blockchain." International Computer Network Security 13.2 (2021). & Use in Journal of Information
[6] Aumasson, Jean-Philippe, et al. "Quark: A lightweight hash." Journal of cryptology 26.2 (2013): 313-339.
[7] Aumasson, Jean-Philippe, Simon Knellwolf, and Willi Meier. "Heavy Quark for secure AEAD." DIAC-Directions in Authenticated Ciphers(2012). S.Rollins and Z.Xu, Peer to Peer Computing, HP Laboratories Palo Alto HPL-2002-57, March, 2002.
[8] Meuser, Tobias, Larissa Schmidt, and Alex Wiesmaier. "Comparing Lightweight Hash Functions–PHOTON & Quark." Download. Hrz. Tu-Darmstadt. De (2015).
[9] Bogdanov, Andrey, et al. "SPONGENT: A lightweight hash function." International workshop on cryptographic hardware and embedded systems. Springer, Berlin, Heidelberg, 2011.