## Slide 1: No Silver Bullet: Optimized Montgomery Multiplication on Various 64-bit ARM Platforms
Hwajeong Seo1, Pakize Sanal2, Wai-Kong Lee3, Reza Azarderakhsh2
1Hansung University, 2Florida Atlantic University, 3Gachon University
21. 08. 13.

## Slide 2
Related Work
Proposed Method & Evaluation
Introduction
Conclusion

## Slide 3: Motivation
High-speed implementation of cryptography is important to achieve high availability.
In order to improve the performance, the core operation of cryptography should be implemented efficiently.
  e.g. public key cryptography  multiplication
Previous works devoted to improve the performance only on specific platforms.
In this paper, we point out that the performance of implementation is varied depending on platforms w/ same base architecture (e.g. ARM).  We should carefully select the proper algorithm on specific platform!

## Slide 4: Contribution
Optimized Montgomery multiplication on ARM64 architecture
  w/ Karatsuba algorithm and instruction sets of ARM64
Efficient implementation of CSIDH on ARM64 architecture
  Full protocols of CSIDH-P511 on 64-bit ARM Cortex-A and Apple A
In-depth performance evaluation on ARM64 architecture
  Analysis of Montgomery multiplication and CSIDH on both architectures
  Karatsuba is not the best solution across all ARM64 architectures

## Slide 5: Target Platform – ARM64
Almost all smartphones based on ARM architecture
Modern smartphone supports 64-bit ARMv8

## Slide 6: Target Platform – ARM64
32-bit mode (AArch32) & 64-bit mode (AArch64)
64-bit ARM & 128-bit NEON registers and instruction sets
Crypto (AES and SHA) operation

## Slide 7: Multiplication on ARM64
a0
b0
a0b0
a0b0
X0
X1
X2
64 bits
X3
UMULH
a0
b0
a0b0
a1b0
X0
X1
X2
64 bits
X3
MUL

## Slide 8: Montgomery Multiplication
Replacing expensive divition into multiplication.
  Division 100~1000 multiplication

## Slide 9: Comparison of Montgomery Multiplication on ARM64
This is the first Montgomery reduction implementation with Karatsuba algorithm.
Application is CSIDH, RSA, and ECC.

## Slide 10: Karatsuba-Ofman Algorithm
Number of partial product
The product of two n-bit integers and
512-bit multiplication case
  2-level Karatsuba (128  256  512)
School-book | Karatsuba-Ofman
School-book | Karatsuba-Ofman

## Slide 11: Karatsuba + Montgomery Multiplication ( 1 / 2 )
Read-write dependency avoidance
Steps 1 and 3 are performed in Algorithm 2.
Steps 2 and 4 are performed with Karatsuba.
Register utilization

## Slide 12: Karatsuba + Montgomery Multiplication ( 2 / 2 )
512-bit Montgomery multiplication
  2-level Karatsuba multiplication  hybrid reduction (1-level Karatsuba)
Acceleration of public key cryptography
  CSIDH-P511 based on the proposed 512-bit Montgomery multiplication
  Conventional public key based on random prime (RSA and ECC) can be accelerated with the proposed method.

## Slide 13: Evaluation (Target Platforms)
ARM processors are largely divided into Cortex-A and Apple A.
Previous works mainly evaluated on Cortex-A processors rather than Apple A.
In this work, we evaluated same codes on both platforms.

## Slide 14: Evaluation ( 1 / 2 )
Cortex-A series show higher MUL/ADD ratio than Apple A processor.
Karatsuba algorithm requires many addition operations than schoolbook.

## Slide 15: Evaluation ( 2 / 2 )
[8] is schoolbook method and optimized version is Karatsuba.
On Cortex-A, Karatsuba approach shows better than schoolbook.
However, schoolbook is better than Karatsuba on Apple A.

## Slide 16: Conclusion
Achievements
  Optimized Montgomery multiplication w/ Karatsuba and specific instructions.
  However, Apple A processors w/ low multiplication latency achieved the better performance with the schoolbook method.
  The implementation should be evaluated on various ARM platforms for fair comparison and practicality.
Future works
  Improving the Microsoft-SIDH library on Apple A processors by utiizing the schoolbook.
  Investigating the multiplication method for various integer lengths.
  Public domain (https://bit.ly/3rOLv4H)!