## Slide 1: Detecting Block Cipher Encryption for Defense against Crypto Ransomware on Low-end Internet of Things
Hyunji Kim, Jaehoon Park, Hyeokdong Kwon, Kyoungbae Jang,
Seungju Choi, and Hwajeong Seo
khj1594012@gmail.com

## Slide 2
Crypto Ransomware
Previous Works
Proposed Method
Evaluation
Conclusion

## Slide 3: Crypto Ransomware
A crypto ransomware encrypts files of victims using block cipher encryption.
The ransomware virus has became a massive threat of people with digital devices.
  It is necessary to defend against ransomware.
ransomware
  1) The hacker requests a ransom for encrypted files
  from the victim.
Victims
Hackers
  2) The victim pays the ransom and receives a secret key.
  3) The victim recovers the encrypted file using a secret key.

## Slide 4: Previous Works
Features | Grobert et al. (2011) | Lestringant et al. (2015) | Kiraz et al. (2017) | This work (2020)
Target | Block & PKC | Block Cipher | PKC | Block cipher
Analysis | Dynamic | Static | Dynamic | Static
Method | Heuristics | Data graph flow | System monitor | Deep learning
Machine | Desktop | Desktop | Desktop | Microcontroller

## Slide 5: Proposed Method
  1. Crypto ransomware
  Cryptographic process
binary
file
(lss, hex)
2. Static analysis
Binary file
Instruction, Opcode
3. Deep learning based detection of block cipher encryption
Learning the encryption pattern through images
Convolutional Neural Networks (CNN)
4. Low-end 8-bit AVR microcontrollers
8-bit AVR ATmega128
Lightweight block cipher library and general firmware
GNU AVR-GCC compiler

## Slide 6: Proposed Method
  *instruction (operand + opcode)

## Slide 7: Convert instruction and opcode into image
Instruction and opcode extraction from binary file (.lss)
Image from binary

## Slide 8: Deep learning
Image from binary
convolution layer
pooling layer
Feature extraction and enhancement
Fully connected
layer
HIGHT, LEA (ARX)
general firmware
crypto ransomware
general firmware
Classification and detection
Training
phase
Detecting
phase

## Slide 9: Training phase
Repeat convolution and max pooling operation
  convolution : feature extraction
  max pooling : feature enhancement
  Learning the operation types and patterns of the encryption process
image from binary
convolution layer
pooling layer
Feature extraction and enhancement

## Slide 10: Ransomware detection phase
Detecting block cipher encryption for defense against crypto ransomware
  algorithm : AES, PRESENT HIGHT, LEA, general firmware
  architecture : SPN, ARX, general firmware
  Classified as the label with the highest probability
fully connected
layer
HIGHT, LEA (ARX)
general firmware
crypto ransomware
general firmware
classification and detection
Notes: Finally, it is classified as ransomware (block cipher) and general firmware

## Slide 11: Model and Hyper parameters
Inception-v3 (pretrained weights) + 3 fully connected layers
   To adjust the classication problem
Categorical crossentropy and Softmax
  Multi-class classification
Set the optimal hyper parameter through grid search.

## Slide 12: Dataset
Block cipher
  Cryptographic modules written in C language among implementations of FELICS (Fair Evaluation of Lightweight Cryptographic System)
General firmware
  From AVR packages
On 8-bit AVR ATmega128
Unbalanced dataset
  macro and micro average
*FELICS : Fair Evaluation of Lightweight Cryptographic System

## Slide 13: Dataset
SPN has a more complicated structure than ARX.
Images differ depending on the type or pattern of instructions used.
SPN
ARX
General

## Slide 14: Instruction-based vs Opcode-based
operand
opcode
The opcode is same, but the operand is slightly different.
  *instruction (operand + opcode)

## Slide 15: Instruction-based vs Opcode-based
Opcode-based
  Stable performance for untrained data
  The standard deviation for micro and macro is 0.12.
  The standard deviation of the metrics for each experiment is also less opcode based.
*F-measure : a harmonic mean of precision and recall
*micro : considering the number of data belonging to each class (for each data)
*macro : considering all classes with the same weight (for label)

## Slide 16: GCC optimization option (O0, O1, O2)
The extracted opcode is slightly different depending on the optimization option.
O0 : Best performance for validation dataset, but not best for test dataset
O1 : Stable and best generalization performance for test dataset (untrained data)

## Slide 17: Frequently used instructions for each architecture
SPN
  S-box operation  the pattern of , memory access (, )
ARX
  Addition, Rotation, and eXclusive-or (arithmetic and logical operations) 
General
  interrupt function, I/O register, branch statements 

## Slide 18: SPN vs ARX vs General
Cryptographic algorithms of the same architecture have similar patterns.
  incorrect classification between algorithms with the same architecture
Classification for each architecture (SPN, ARX and General firmware, not each algorithm) achieved better performance.
It accurately predicted test data in optimization option O1.
Notes: (in previous experiment  잘못분류된경우는 대부분 그 .. 같은 구조끼리…였음

## Slide 19: Conclusion
Contribution
  Deep learning based crypto ransomware detection for low-end microcontrollers
  Experiments with several options for high accuracy
Future work
  Test and evaluate our method using the real ransomware samples.